## Slide 1: Internship SDSoC
Andrew Maclellan

## Slide 2: Introduction
What is SDSoC?
  Software Defined System on Chip.
  Accelerate software functions (C/C++) within the FPGA on Zynq devices.
  Aimed at software engineers with limited hardware knowledge.
  Runs on top of Vivado, Viavado HLS, and SDK.

## Slide 3: SDSoC Structure
Platform created in Vivado and linked to SDSoC.
C/C++ program written in SDSoC.
Selected functions are built into hardware.
Run on device through JTAG or booted from SD card.

## Slide 4: SDSoC Features
Hardware acceleration
Automatically creates boot files for baremetal, linux, and FreeRTOS.
Vivado HLS pragmas. (Pipeling, unrolling etc…)
Estimation Reports (Comparing software only to hardware accelerated).
Axi Performance Interface.

## Slide 5: Learning
Zynq Book.
2 day training course SDSoC (Rutherford Appleton Laboratory).
Creating own platform.
Using HLS pragmas.
Writing software to be synthesisable in hardware.

## Slide 6: Application of SDSoC
Zybo.
Image processing.
Following SDSoC structure.
Program for hardware.
Create filters for:
  Pass-through and colour change.
  Greyscale.
  Average Filter.
  Sobel Filter.

## Slide 7: Platform
Zybo Digilent platform.
HDMI_in, VGA_out, CLKs, GPIO…

## Slide 9: Pass-through

## Slide 10: Pass-through

## Slide 12: Grayscale

## Slide 13: Greyscale
Y = (R * 76) + (B * 150) + (G * 29 + 128) >> 8

## Slide 15: Average Filter

## Slide 16: Average Filter
Z_Average = (Z1 + Z2 + Z3 + Z4 + Z5 + Z6 + Z7 + Z8 + Z9) * 1/9

## Slide 18: Sobel Filter

## Slide 19: Sobel Filter
Gx
Gy

## Slide 20: Sobel Filter
G_mag = ABS(Gx) + ABS(Gy)
https://upload.wikimedia.org/wikipedia/commons/thumb/d/d4/Valve_sobel_(3).PNG/300px-Valve_sobel_(3).PNG

## Slide 21: Sobel Filter
Future implementation:
  Edge thresholding.
Gradient threshold at 100.
>=100 is set as white.
<100 is set as black.

## Slide 22: Hardware implementation
Using HLS pragmas:
Pipeline Unroll
Memory attributes and access patterns

## Slide 23: Any Questions?